## Slide 1: POWER AND EFFICIENCY
Section 12.7

## Slide 2: Power
Rate at which electrons spend their energy when they encounter a load or resistance.
Depends upon two things:
  The greater the _potential difference__ across a load, the _greater_ the __energy___ converted to heat and light.
  The more _electrons passing through a load, the _faster___ the energy is converted.

## Slide 3: Power
Metric Units - One _Watt____ is a rate of converting one _Joule_ of energy to another form per second. P = E/t
Power (W) = Energy/time (J/s)
Power (Watt) = potential difference(volt) x current(ampere)
P = V I

## Slide 4: POWER Analogy
Power is like the total amount of money spent on tickets for a show. The rate at which money is spent at each checkout depends on:
cost per ticket (voltage)
amount of people buying tickets (current)

## Slide 5: Practice Problem
A current of 13.6A passes through an electric baseboard heater when it is connected to a 110V wall outlet. What is the power of the heater?
P = VI
= 110V x 13.6A
= 1496W
The power of the baseboard heater is 1496W

## Slide 6: Efficiency
When we transfer energy from gas, wind, or water into electricity, not all of the energy is transferred into electricity, some is lost in the form of heat___.
This is also true when we transfer the electrical energy back into _sound___, _thermal_, or _chemical_ energy to make our lights and appliances function.
Efficiency is a measure of how much useful energy comes out of a device, compared to how much total energy goes in.

## Slide 7: Efficiency
Most appliances make use of only a portion of the input energy. Some appliances are better at using _more__ of the electrical energy that it receives. They are said to be more _efficient_____.
The joule(J) is a relatively small unit of electrical energy, so energy consumption is often measured in kilowatt.hours (kW.h), derived from the power formula
Power = Energy/time
Energy = Power(kW) x time(h)

## Slide 8: Efficiency
We can calculate the efficiency of an appliance or power plant by comparing the energy output that is useful with the total energy input.
% Efficiency = _useful energy output_ x 100
total energy input

## Slide 9: Practice Problem
Determine the % efficiency of a 60 W fluorescent light bulb that uses 2000J of electrical energy to produce 400J of light energy.
% efficiency = useful energy output x 100
total energy input
= 400J x100
2000J
= 20% efficient
Where did the other 80% go?
Well, a light bulb is designed to provide light so any energy that is not converted to light is not useful energy. Most of the 80% is wasted as heat.

## Slide 10: Efficiency of some common items
Machine | Efficiency
Electric heater | 99%
Home gas furnace | 85%
Wind generator | 60%
Nuclear power plant | 30%
Car engine | 26%
Fluorescent light | 20%
Silicon solar cell | 12%
Steam locomotive | 9%
Incandescent lamp | 2%
Remember, efficiency is based on useful energy, what the machine was intended to do

## Slide 11: Cost of Electricity
All electricity entering your house or apartment is measured using a smart meter. A Smart meter measures the amount of energy entering your house as well as the time of day that it is being used. In Ontario we have different rates for electricity usage, depending on the season and time of day (paused right now during the pandemic THANKFULLY!) When you use an electrical appliance or device, the energy passes through the meter first and is recorded for your bill. Electricity cost is billed as ¢ / kW.h (cents per kilowatt hour)
Cost to operate = energy used x cost of energy
Cost to operate = (power x time) x cost of energy

## Slide 12: Practice Problem
Last summer the school changed from fluorescent bulbs to LED for the lighting of the school. Each of the old ceiling light fixtures had 4 fluorescent bulbs and were replaced with fixtures containing 2 LED’s which provides the same amount of light. Let’s calculate how much money the school will save in a year.
Assumptions:
500 fixtures were replaced
lights are on from 7:00am-7:00pm (12 hours per day/5 day per week/10 months per year)
Fluorescent bulbs are 43W
LED bulbs are 16W
Cost of electricity during school hours is the on-peak rate of 13.4 ¢/kW.h

## Slide 13: Cost to run old Fluorescent Bulbs
Cost per bulb = [power x time] x cost of energy
= [43W x (12h/day x 5day/week x 4week/month x 10month/year)] x 13.4 ¢/kW.h
= [103200W.h/year] x 13.4¢/kW.h (103200W.h/year = 103.2kW.h/year)
= 1382.88 ¢/year = $13.8288/year per bulb (there are 2000 bulbs)
= $27657.60/year when using fluorescent bulbs

## Slide 14: Cost to run new LED Bulbs
Cost per bulb = [power x time] x cost of energy
= [16W x (12h/day x 5day/week x 4week/month x 10month/year)] x 13.4 ¢/kW.h
= [38400W.h/year] x 13.4¢/kW.h (38400W.h/year = 38.4kW.h/year)
= 514.56 ¢/year = $5.1456/year per bulb (there are 1000 bulbs)
= $5145.60/year when using LED bulbs

## Slide 15: Savings per Year
Cost savings = cost of using fluorescent – cost of using LED
= $27657.60/year - $5145.60/year
= $22512.00/year Not too bad…

## Slide 16: Practice
1) Power Practice Problems (end of the note)
2) Read Section 12.7 p.530-535 in your text.
3) page 535 #5,6,7
4) Take the Check Your Understanding Quiz